## Slide 1
Retrieving Extreme wind speeds using C-band instruments
Gerd-Jan van Zadelhoff, Ad Stoffelen, P. Vachon, J. Wolfe, J. Horstmann, M. Belmonte Rivas, F. Fois
van Zadelhoff et al. (amt-7-437-2014)

## Slide 2
MetOP Second Generation
The MetOP-SG series will be launched in 2020+
One instrument on board is a vertical co-polarization (VV) C-band scatterometer (SCA), similar to ASCAT.
An innovation on ASCAT-SG is the inclusion of cross-polarization (VH) channels on the scatterometer mid beams to retrieve extreme winds.
The goal of the present work was to provide a scientific background to assist in the decision-making process on including the VH channels to the ASCAT-SG instrument.
We present a cross-polarization Geophysical model function (VH-GMF) based on RadarSAT2 SAR data.

## Slide 3: Zhang et al. 2011
Wind speed vs. cross polarization
Vachon et al.(2011) & Zhang et al. (2011) used RadarSat-2 SAR data, collocated with in situ buoy measurements to check for wind dependence
The VH signals (up to ~20 m/s) appear linear in dB
No clear incidence and azimuth angle dependence are apparent in their data.
In this work we look into the VH dependence at higher wind speeds (>20m/s)

## Slide 4
19 images of 13 different Hurricanes (2008-2011)
The VH band shows a sharp defined ‘eye’, no apparent incidence angle or rotation angle dependence.
Hurricane images RadarSat-2
Hurricane Earl [September 02 2010, 22:59:20]

## Slide 5
Evaluating VH signals using wind speed information
Two eye-position corrected velocity sources have been used in this research to create a VH-GMF:
  SFMR velocities from
  NOAA Hurricane flights
  ECMWF forecasts:+3,6, ..
NB: HWIND was tested, but explained least variance among all others: SFMR, ECMWF and RadarSat VH
The NOAA best track maximum wind speed estimates are subsequently used to validate the main results.
VV, HH and VH

## Slide 6
Collocation and comparison of SFMR & RadarSAT-2
Not all Hurricanes have collocated SFMR data (18 legs; 8 hurricanes)
Separate each NOAA flight in separate flight legs
Collocate each leg separately with RADARSAT-2 image

## Slide 7
Combining all available SFMR data
There seems to be a incidence angle dependence in the SFMR data (blue 20o  red 48o)
More comparison data is required  ECMWF wind speeds are used for this

## Slide 8: Wind direction dependence
VV
VH
Correct both the VH and VV signals for their incidence angle dependence and check for a wind direction pattern

## Slide 9: Collocation with ECMWF forecasts
A total of 19 RADARSAT-2 dual polarized SAR images (VV and VH) were acquired between 2008 and 2011.
The combined distribution is well structured (relatively small width; corr. 0.85) but shows a (weak) incidence angle dependence

## Slide 10: Wind direction dependence
Cross polarization signals show no wind direction dependence
VV
VH

## Slide 11
Creating a VH-GMF
SFMR
ECMWF
SFMR-VH and ECMWF-VH distributions look very similar
There is a change in slope around 20m/s
VH-GMF:

## Slide 12: Calibrating U10 in Hurricanes ?
Vachon + SFMR
Vachon 2011
VH-GMF
SFMR track
Vachon
VV-GMF
ECMWF
ECMWF

## Slide 13: Calibrating U10 in Hurricanes ?
VH-GMF
Vachon
VV-GMF
ECMWF
SFMR

## Slide 14
Comparing the NOAA best track estimate (max. 1-minute sustained surface wind speed) versus the averaged VH-signals of the 0.995 and 0.9995 percentile values.
+12 hours
-12 hours

## Slide 15
Comparing the NOAA best track estimate (max. 1-minute sustained surface wind speed) versus the averaged VH-signals of the 0.995 and 0.9995 percentile values.
Cross polarization data can be used to retrieve the ‘near real time’ Maximum wind speed.
Cross polarization data appears not to saturate up to ~60m/s wind speeds

## Slide 16: SFMR?
CMOD5n winds are lower than SFMR (VV pol)
CMOD5 winds are equal to buoy winds for 15 to 20 m/s; which to trust?
SFMR winds go up when it rains; NOAA is recalibrating

## Slide 17: SFMR?
Wind speed bias and rain rate appear correlated

## Slide 18: ASCAT and SMOS scales
30 40 50
y (x) regressed
30 40 50 60 70

## Slide 19
ASCAT eye wall

## Slide 20: ASCAT – QuikScat
Corrected at KNMI

## Slide 21: Conclusions
An additional cross polarization (VH) channel on ASCAT-SG will retrieve wind speeds up to at least 45 m/s (based on available SFMR data)
The VH wind speed dependence shows a different relationship in the low&strong wind speed regime(U10<20m/s) compared to the strong&severe wind speed regime(U10>20m/s)
The VH signals show a modest incidence angle dependence and negligible wind direction dependence in the VH signals
There is a strong correlation between the highest VH measurements within a hurricane SAR image and the one-minute maximum sustained wind speeds from the NOAA best track product up to 60 m/s. This correlation can be described by a linear relationship and can be used for TC guidance
An operational satellite with a VH channel will be able to retrieve in near real time the one-minute maximum sustained wind speed from a hurricane or typhoon, and an assessment of the spatial wind speed distribution
Both VH and extreme wind measurements need more attention in calibration at appropriate spatial resolution

## Slide 22
Scatterometers measure the radar backscatter from the ocean
The return depends on the roughness of the ocean and the incidence angle
The roughness of the ocean can be directly related to the (10 meter equivalent-neutral) wind speed
The backscatter is strongly dependent on the wind direction (upwind >> crosswind)
The signal saturates at about 40m/s
Scatterometers & wind speed
Zhang et al. 2011
www.knmi.nl/scatterometer/cmod5