## Slide 1: Sea State Influence on SFMR Wind Speed Retrievals in Tropical Cyclones
Heather Holbach1,2,3, Mark Bourassa1, and Brad Klotz3
1 Florida State University, 2NGI, 3NOAA/AOML/HRD
International High Winds Workshop
Exeter, UK
November 16, 2016
We acknowledge Mark Powell, Frank Marks, and the pilots and crew at NOAA AOC. Research supported by NASA JPL (036683), NOAA (031132) and NGI.

## Slide 2: SFMR Wind Speed Retrieval
Successful retrievals rely on understanding the relationship between ocean surface brightness temperature and wind speed
  Many other factors can influence the ocean surface brightness temperature besides wind speed
    Sea state
    Viewing angle
      Wind direction
    Sea surface temperature

## Slide 3: Hurricane Wave Characteristics
Swell:
  More dominant in inner core (Wright et al. 2001, Hwang 2016)
  Cross swell (wrt wind direction) reduces white capping (Goddijn-Murphy et al. 2011) and limits wave breaking (Holthuijsen et al. 2012)
Fig. 3 Holthuijsen et al. (2012)

## Slide 4: Hurricane Wave Characteristics
Wind waves:
  More dominant in outer region (Wright et al. 2001, Hwang 2016)
  Hwang (2016):
    Tallest in front-right sector
    Longest wavelength in front-right and front-left sectors
    Smallest (height) and shortest wavelength in rear sector
    Steepest waves in front-right or rear sector.
Fig 2 Hwang (2016)
Left
Back
Right
Inside 30km
from center
X

## Slide 5: Methodology
200
100
0
-100
-200
Along Storm Track Distance (km)
Cross Storm Track Distance (km)
200
100
0
-100
-200
Level flight data collocated with a dropsonde in a hurricane between 2010 and 2015
where
Wind-induced emissivity is calculated by subtracting smooth surface emissivity, the atmospheric, and cosmic emissivity
Wind-induced emissivity difference is 4.74 GHz SFMR – model fit from Klotz and Uhlhorn (2014)
Storm Motion
Azimuth Angle

## Slide 6: Wind-Induced Emissivity vs. Wind Speed
422 collocation pairs with rain rate less than 10 mm/hr
At 20 m/s, 0.005 change in wind-induced emissivity results in 1.6 m/s wind speed change
At 40 m/s, 0.005 change in wind-induced emissivity results in 0.9 m/s wind speed change
0.25
0.20
0.15
0.10
0.05
0.00
Wind-Induced Emissivity
60
50
40
30
20
10
0
Wind Speed (m/s)
RR < 2 mm/hr
2 mm/hr ≤ RR < 10 mm/hr
10 mm/hr ≤ RR < 20 mm/hr
RR ≥ 20 mm/hr
Model Fit

## Slide 7: Wind-Induced Emissivity Difference
0.00
-0.05
Wind-Induced Emissivity Difference
300
0
100
200
Storm Relative Azimuth Angle (°)
0.05
10 to 20 m/s
300
0
100
200
Storm Relative Azimuth Angle (°)
20 m/s +
(4.74 GHz SFMR – Model)

## Slide 8: 20 m/s + (Radius ≤ 50 km vs Radius > 50 km)
n (R ≤ 50 km) = 97
n (R > 50 km) = 141
Lines: Running medians of 30° azimuthal bins
0.05
0.00
-0.05
Wind-Induced Emissivity Difference
300
0
100
200
Storm Relative Azimuth Angle (°)
a
300
0
100
200
Storm Relative Azimuth Angle (°)
b
0.01
0.00
-0.01
0.02
-0.02
0.03
R ≤ 50 km
R > 50 km
All
R ≤ 50 km
R > 50 km
All

## Slide 9: Storm Relative Azimuthal Asymmetry and Swell
Lower Emissivity
Higher Emissivity
Higher Emissivity
Fig. 3 Holthuijsen et al. (2012)
270
0
90
180
Storm Relative Azimuth Angle (°)
0.01
0.00
-0.01
0.02
-0.02
0.03
R ≤ 50 km
R > 50 km
All
Wind-Induced Emissivity Difference

## Slide 10: Conclusion
  Following and opposing swell increases wind-induced emissivity measured by SFMR
    Cross swell decreases it
  Wind waves and swell combination in outer regions of storm dampen the asymmetry
  These results are further evidence that directional wind and wave interactions modify ocean surface stress and must be considered in model development

## Slide 11: SFMR Update
SFMR data from 1998 to 2014 have been reprocessed using the current algorithm (Klotz and Uhlhorn 2014)
In the process of updating the data files on the HRD website
  Blog post and message on HRD website will be posted when complete
These data will be used in Jonathan Vigh's FLIGHT+ dataset

## Slide 12: Collocation Restrictions
WL150 surface adjusted wind speed and 10-s avg. SFMR wind speed greater than 10 m/s
Located greater than 5 km and less than 200 km from storm center
Dropsonde cannot travel more than 9 km radially from the launch location
Aircraft roll angle could not exceed 10°
Total of 580 collocation pairs
Storm Motion
Azimuth Angle