## Slide 1
- Aeolus – The Atmospheric Dynamics Mission
Ad.Stoffelen@knmi.nl
Industrial Aeolus Team
ESTEC, ESRIN, ESOC A-teams
Aeolus MAG
Aeolus L1 and L2 team
Aeolus Cal/Val teams

## Slide 2: Outline
ADM-Aeolus scientific motivation and objectives
Mission and instrument characteristics
Instrument and project status
Processing and data products
Mission CAL/VAL and campaigns
Conclusions

## Slide 3: Bus?
planetary waves
low pressure systems
storms, fronts
orographic circulations
mature systems
developing systems
boundary layer
10 100 1000 10.000 H [km] Shower Front Storm Climate zone World
Mist Cloud layer Rain colomn 10 V [m] 100 1000 10.000
Development
Wind determines weather evolution
Temperature and pressure for weather evolution
Rossby limiet voor 45 N (of 45 Z)
Fast
Slow
So:
Measure wind
With more spatial detail
More often, AND
More accurately

## Slide 4
Differences in (re)analysis data
Baker et al., 2014
NCEP
Tropics
Oceans
Upper air

## Slide 5
200 mb winds 15 Mar 2014
A poor forecast
Tropics
Tropical errors affect European forecasts on the predictable range
Amplification of error by moist convection
Day 6
Day 5
Day 4
Day 2
D3
Error Propagation
Notes: But on any given day some forecasts can be poor!
ECMWF suffered a (mercifully extremely rare) data corruption problem on Saturday 28 June, which I’ll ask Florence just to say something about briefly.
If we come back to an occasion where the issue was meteorological rather than data corruption. On 15 March 2014 ECMWF had its worst 6 day forecast for over a decade!
Forecast had a ridge over western Europe and a trough over central Europe whereas in fact the flow was essentially zonal.
Largest EDA spread on the globe was over the eastern tropical Pacific and the signal of this reached Europe 6 days later.
2-3 days into the forecast strong convection appeared over southern U.S. and amplified the propagating error.
This indicates the importance of improved observations of tropical winds and the launch of the Aeolus satellite next year should help. It also suggests that the process of amplification of errors by convection needs to be understood better.

## Slide 6
Unbalanced
Full field
Absolute analysis increments u150
Balanced
Unbalanced
18UTC average for Sept-Nov 2015
Dynamical errors in the tropics and in moist convection are mostly unbalanced and 3D winds are needed to observe them, hence Aeolus

## Slide 7: Hi-res radiosonde shear
ECMWF winds agree very well with sondes
Vert. shear in ECMWF model 2-3 times lower, however
Large tropical tropopause shear gradient
Shear determines mixing of air, air interaction, cloud dyn., ..
Houchi et al. 2010
RAOB
ECMWF
ECMWF
RAOB
Tropics

## Slide 8
Importance for winds for climate applications
Example of Grand Challenges of the World Climate Research Programme
  Understanding coupling Troposphere and Stratosphere dynamics and its impact on climate variability
  Role of dynamically driven cloud circulation interactions for climate sensitivity
Courtesy S. Bony, B. Stevens

## Slide 9
Importance of winds for climate applications
Example of Grand Challenges of the World Climate Research Programme
  Understanding coupling Troposphere and Stratosphere dynamics and its impact on climate variability
  Role of dynamically driven cloud circulation interactions for climate sensitivity
Tropical ozone strongly impacted by UTLS dynamics (e.g. convection, gravity waves, planetary waves)
Role of dynamics in formation of ozone holes in Arctic
Energy exchange atmosphere and ocean, …

## Slide 10: Aeolus Mission Objectives
Scientific objectives
To improve the quality of weather forecasts
To advance our understanding of atmospheric dynamics and climate processes
Explorer objective
Demonstrate potential for operational use of space-based Doppler Wind LIDARs (DWL)
Observations
Global measurements of single line-of-sight wind profiles in the troposphere and lower stratosphere
Spin-off products are atmospheric extinction and backscatter profiles
Payload
ALADIN: Atmospheric LAser Doppler INstrument

## Slide 11: What will we see?

## Slide 12: Cloud layer statistics from radiosondes
Aeolus height bins are typically 1 km
But, 1/3 of cloud layers are thinner than 400m
Such layers cause non-uniform Mie backscatter and extinction
Mean backscatter height will be uncertain
Wind and wind shear will be biased (mean shear = 4 m/s per km height)
Advanced retrieval methods will be needed
Wei et al., 2014

## Slide 13: Cloud/aerosol layer inside Aeolus bin
Aeolus wind error can be large depending on (i) bin size, (ii) cloud/aerosol layer location inside the Aeolus bin, (iii) layer size, (iv) layer transmission and (v) wind-shear over the bin
30 m/s
1 km
20 m/s
25.0 +0.0 25.44 +0.44
30.0 +10.0 25.10 +0.10
20.0 -10.0 25.07 +0.07
27.5 +2.5 25.36 +0.36
27.5 +2.5 25.30 +0.30
2-way cloud layer transmission: 0.7
10 m/s /km wind wind shear
Mie error
Rayleigh error
Mie wind errors are very sensitive to
atmospheric heterogeneity !!
Notes: ((1-f)*((30)+(10*f+20))/2+t*f*((10*f+20)+20)/2)/(1-f+t*f); t=2-way cloud transmission, f = cloud location in bin in [0,1]

## Slide 14: RMSE wind error
Mie Rayleigh
m/s
m/s
cloud layer
z

Bin height
Rayleigh HLOS insensitive to z
c can be obtained from Aeolus optics
Rayleigh winds are under control
Mie H however sensitive to z

## Slide 15: Polar Stratospheric Clouds
Quite a lot over Antarctic in August and Arctic in January
30 km
15 km
Mainly sampled by molecular channel

## Slide 16
Forward Engineering
Mission success depends on reverse engineering generally (in cal/val)
KNMI developed a Chain of Processors to aid cal/val feedback process

## Slide 17
QRT coverage
Dumps to Svalbard X-band station
Courtesy KSAT
QRT service: delivery of L1B BUFR to users within 30 min.
Explore possibility of L2B BUFR delivery to users in QRT/NRT to enable regional short-range forecasting benefit
Quasi Real-Time (QRT)

## Slide 18: Prospect based on HiRLAM operations
~70-100% of Aeolus QRT L2B winds can be used in current HiRLAM implementations
< 50% of Aeolus NRT L2B winds can be used in HiRLAM
  These numbers vary for other NRT and QRT specs.
There is a general tendency to 3-h/1-h cycling and fast cut-off in the coming years to better exploit fast observations (like EARS), increasing the need for QRT delivery in regional NWP

## Slide 19: What if Aeolus is a success?
13th International Winds Workshop, Monterey, 27 June - 1 July 2016
Draft report to WMO CGMS from Working Group 2 (WG2): Data Assimilation
6. New satellite mission proposals
There continues to be an unmet requirement of wind profile observations with sufficient global and temporal coverage. The group is looking forward to Aeolus data which will give profiles of line-of-sight winds, but notes that currently there is no secure follow-on mission. Some proposed missions with potential have been presented at the workshop.
Recommendation to space agencies: to implement satellite missions that allow the provision of wind profile / dynamical information with global coverage (e.g., DWL, hyperspectral IR with high temporal frequency and spatial resolution). .
Low-cost pre-design study?

## Slide 20: Summary
Expectations of the impact of Aeolus remain high
Main improvements are expected in the tropical dynamics, the upper air and in the representation and parameterisation of dynamical processes, such as gravity wave drag, (moist) convection and turbulence
Data processing studies have been performed and errors assessed; subtleties in optical and wind processing appear important, certainly near clouds
A chain of calibration and wind processors is developed
To support the operational meteorological community, QRT/NRT ingestion is facilitated by ESA in the Ground Segment up to L1B
The cal/val phase will be an exiting time where the A-team looks forward to!
Aeolus is a demonstrator in preparation for a follow-on

## Slide 21
An artist’s view of Aeolus in flight
http://www.esa.int/livingplanet/ADM-Aeolus